## Slide 1: ECE330 SoC Design Final Report
Kyritsis Spyridon, Konstantina Topali

## Slide 2: Presentation Overview
Functional Verification
Project Description
Logic Synthesis
Placement & Routing
Post PnR
Timing & Power Reports
Post PnR
Functional Verification

## Slide 3: Description
Our project is to apply the ASIC design flow and create an AES Encoder/Decoder system with error detection capabilities
Design source files
  Author: Joachim Strömbergson
  https://www.librecores.org/JoachimS/aes-128256
  https://github.com/secworks/aes

## Slide 4: Source Files
The project consists of mutually exclusive encipher and decipher blocks
  Can be separated and function independently
The project’s source files include:
  The RTL files for each submodule of the core’s implementation
  Separate testbenches for each module
  High-level test models for the AES algorithm parts
    Written in Python

## Slide 5: AES Algorithm
The AES (Advanced Encryption Standard) consists of 4 distinct operations
  AddRoundKey
  SubBytes
  ShiftRows
  MixColumns
The AES encryption and decryption algorithms are mirror images
  For a given key the inverse operations are easily defined and carried out

## Slide 6: Block Diagram
Our project connects the encipher and decipher blocks in series
  Our goal is to verify that the encryption and decryption modules function correctly
  For the purposes of this project, we will only focus on 128-bit keys

## Slide 7: Presentation Overview
Functional Verification
Project Description
Logic Synthesis
Placement & Routing
Post PnR
Timing & Power Reports
Post PnR
Functional Verification

## Slide 8: Python Model Results
Contains tests for the AES128/256 implementations
  Runs 4 different tests for all implementations
  Runs tests for both encryption and decryption
  Analytic results for each step of the algorithm

## Slide 9: Python Model Results
….

## Slide 10: Behavioural Simulation
For the behavioural simulation we will be using Cadence© Incisive™
  We will be using an automated testbench
  Compare our results VS Python Model
  Test vectors copied from the following NIST documents:
    NIST SP 800-38A:
    http://csrc.nist.gov/publications/nistpubs/800-38a/sp800-38a.pdf
    NIST FIPS-197, Appendix C:
    https://nvlpubs.nist.gov/nistpubs/FIPS/NIST.FIPS.197.pdf

## Slide 11: Behavioural Simulation

## Slide 12: Behavioural Simulation
….

## Slide 13: Presentation Overview
Functional Verification
Project Description
Logic Synthesis
Placement & Routing
Post PnR
Timing & Power Reports
Post PnR
Functional Verification

## Slide 14: Logic Synthesis Methodology
Top-Down Logic Synthesis
Behavioral Simulation
Bottom-Up Logic Synthesis
Post Synthesis Simulation w/o delay annotation
Post Synthesis Simulation w/ delay annotation
Pareto Curve Creation

## Slide 15: A lesson through…

## Slide 16: Behavioral Simulation
Top-Down Logic Synthesis
Behavioral Simulation
Bottom-Up Logic Synthesis
Post Synthesis Simulation w/o delay annotation
Post Synthesis Simulation w/ delay annotation
Pareto Curve Creation
We tested our design be comparing its waveforms output to a software model
The outputs match

## Slide 17: Problems (cont.)
In order to fix this mess
We switched to a newer version of Design Compiler™
  Well…

## Slide 18: Top-Down Logic Synthesis
Top-Down Logic Synthesis
Behavioral Simulation
Bottom-Up Logic Synthesis
Post Synthesis Simulation w/o delay annotation
Post Synthesis Simulation w/ delay annotation
Pareto Curve Creation
We created a top-down TCL script with clock_period starting from 1 ns to 10 ns

## Slide 19: Bottom-Up Logic Synthesis
Top-Down Logic Synthesis
Behavioral Simulation
Bottom-Up Logic Synthesis
Post Synthesis Simulation w/o delay annotation
Post Synthesis Simulation w/ delay annotation
Pareto Curve Creation
Then we created bottom-up TCL scripts with clock_period starting from 1 ns to 10 ns

## Slide 20: Bottom-Up Logic Synthesis
Top-Down Logic Synthesis
Behavioral Simulation
Bottom-Up Logic Synthesis
Post Synthesis Simulation w/o delay annotation
Post Synthesis Simulation w/ delay annotation
Pareto Curve Creation
We created a bash script in order to automate the bottom-up synthesis for each clock_period

## Slide 21: Problems
This makes no sense
Apparently, it goes away if the reset is synchronous for some reason…

## Slide 22: Post Synthesis Simulation w/o delay annotation
However, problems still occurred after the reset was fixed
Apparently, the issue is fixed if we use
  compile -map_effort high
  No clock gating
Pareto Curve Creation
Top-Down Logic Synthesis
Behavioral Simulation
Bottom-Up Logic Synthesis
Post Synthesis Simulation w/o delay annotation
Post Synthesis Simulation w/ delay annotation

## Slide 23: Top-Down and Bottom-Up Logic Synthesis
Pareto Curve Creation
Top-Down Logic Synthesis
Behavioral Simulation
Bottom-Up Logic Synthesis
Post Synthesis Simulation w/o delay annotation
Post Synthesis Simulation w/ delay annotation
The results are positive

## Slide 24: Top-Down Synthesis – Area.txt

## Slide 25: Top-Down Synthesis – Power.txt

## Slide 26: Top-Down Synthesis – Timing.txt
For 10ns clock_period
  Slack is MET

## Slide 27: Bottom-Up Synthesis – Area.txt

## Slide 28: Bottom-Up Synthesis – Power.txt

## Slide 29: Bottom-Up Synthesis – Timing.txt
For 10ns clock_period
  Slack is MET

## Slide 30: Pareto Curves - Top-Down Synthesis
Top-Down Logic Synthesis
Behavioral Simulation
Bottom-Up Logic Synthesis
Post Synthesis Simulation w/o delay annotation
Post Synthesis Simulation w/ delay annotation
Pareto Curve Creation
Area vs Time
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
AREA (cells) | 33171.7955 | 30377.7315 | 30109.3375 | 30138.5975 | 30093.3775 | 30153.7595 | 30129.0215 | 30062.5215 | 30341.0235 | 31396.5115

## Slide 31: Pareto Curves - Top-Down Synthesis
Top-Down Logic Synthesis
Behavioral Simulation
Bottom-Up Logic Synthesis
Post Synthesis Simulation w/o delay annotation
Post Synthesis Simulation w/ delay annotation
Pareto Curve Creation
Power vs Time
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
POWER (uW) | 15963 | 8030.4 | 5404.4 | 4094.7 | 3305.6 | 2782 | 2408 | 2128.2 | 1910.6 | 1739.3

## Slide 32: Pareto Curves - Top-Down Synthesis
Top-Down Logic Synthesis
Behavioral Simulation
Bottom-Up Logic Synthesis
Post Synthesis Simulation w/o delay annotation
Post Synthesis Simulation w/ delay annotation
Pareto Curve Creation
Slack vs Time
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
TIMING (ns) | -0.37 | 0 | 0.5 | 1.23 | 2.34 | 3.38 | 4.25 | 5.28 | 6.35 | 7.63

## Slide 33: Pareto Curves - Bottom-Up Synthesis
Top-Down Logic Synthesis
Behavioral Simulation
Bottom-Up Logic Synthesis
Post Synthesis Simulation w/o delay annotation
Post Synthesis Simulation w/ delay annotation
Pareto Curve Creation
Area vs Time
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
AREA (cells) | 32799.1295 | 30220.7915 | 30172.9115 | 30172.9115 | 30171.8475 | 30166.5275 | 30165.4635 | 30165.4635 | 30169.7195 | 30172.3795

## Slide 34: Pareto Curves - Bottom-Up Synthesis
Top-Down Logic Synthesis
Behavioral Simulation
Bottom-Up Logic Synthesis
Post Synthesis Simulation w/o delay annotation
Post Synthesis Simulation w/ delay annotation
Pareto Curve Creation
Power vs Time
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
POWER (uW) | 15947 | 8035.1 | 5420.1 | 4105.7 | 3317.1 | 2791.3 | 2415.7 | 2134.1 | 1915.1 | 1739.9

## Slide 35: Pareto Curves - Bottom-Up Synthesis
Top-Down Logic Synthesis
Behavioral Simulation
Bottom-Up Logic Synthesis
Post Synthesis Simulation w/o delay annotation
Post Synthesis Simulation w/ delay annotation
Pareto Curve Creation
Slack vs Time
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
TIMING (ns) | -0.37 | 0 | 0.42 | 1.42 | 2.42 | 3.42 | 4.42 | 5.42 | 6.42 | 7.42

## Slide 36: Presentation Overview
Functional Verification
Project Description
Logic Synthesis
Placement & Routing
Post PnR
Timing & Power Reports
Post PnR
Functional Verification

## Slide 37: Floorplanning & Power Planning
37
Placement
Floorplanning & Power Planning
Clock Tree Synthesis
Routing
DRC Fixing
ECO optimizations

## Slide 38: Placement
38
38
Placement
Floorplanning & Power Planning
Clock Tree Synthesis
Routing
DRC Fixing
ECO optimizations

## Slide 39: Placement
39
39
Placement
Floorplanning & Power Planning
Clock Tree Synthesis
Routing
DRC Fixing
ECO optimizations

## Slide 40: Placement
Incremental run was needed to fix DRCs
40
40
Placement
Floorplanning & Power Planning
Clock Tree Synthesis
Routing
DRC Fixing
ECO optimizations

## Slide 41: Placement
Incremental run was needed to fix DRCs
41
41
Placement
Floorplanning & Power Planning
Clock Tree Synthesis
Routing
DRC Fixing
ECO optimizations

## Slide 42: Clock Tree Synthesis
42
42
Placement
Floorplanning & Power Planning
Clock Tree Synthesis
Routing
DRC Fixing
ECO optimizations

## Slide 43: Routing
43
43
Placement
Floorplanning & Power Planning
Clock Tree Synthesis
Routing
DRC Fixing
ECO optimizations

## Slide 44: DRC Fixing
44
44
Placement
Floorplanning & Power Planning
Clock Tree Synthesis
Routing
DRC Fixing
ECO optimizations
Added vias where each power stripe intersects with its respecting powerline to fix the DRCs

## Slide 45: ECO optimizations
45
45
Placement
Floorplanning & Power Planning
Clock Tree Synthesis
Routing
DRC Fixing
ECO optimizations
ECO optimization round was necessary since our design did not meet hold timing

## Slide 46: Final Routed Design

## Slide 47: Presentation Overview
Functional Verification
Project Description
Logic Synthesis
Placement & Routing
Post PnR
Timing & Power Reports
Post PnR
Functional Verification

## Slide 48: Post PnR Timing Reports
Timing report extracted from Synopsys© Primetime™

## Slide 49: Post PnR Power Reports
Power report extracted from Synopsys© PrimePower™

## Slide 50: Presentation Overview
Functional Verification
Project Description
Logic Synthesis
Placement & Routing
Post PnR
Timing & Power Reports
Post PnR
Functional Verification

## Slide 51: Post PnR Functional Verification
We provide Incisive™ with the post-PnR netlist and .sdf file
As we can observe our system functions as expected